## Slide 1: Assembly Language
CS274

## Slide 2: MIPS
The collection of commands in an architecture is called the instruction set.
The instruction set comprises the language for the hardware also known as assembly language
Architectures and therefore assembly languages have evolved as technology has evolved.

## Slide 3: CISC vs. RISC Architecture
CISC: Complex Instruction Set Computer
Earlier Assembly languages tried to use less instructions for a task.
The instructions typically took more than one cycle to execute
Summary: Tailors hardware to the higher level language.
http://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/
http://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/

## Slide 4: CISC vs. RISC Architecture
RISC: Reduced Instruction Set Computer
Instructions did less, but could be combined to achieve the same tasks as the CISC commands.
Each instruction executed on one CPU cycle.
Summary: Tailors language to hardware.
http://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/

## Slide 5: CISC vs. RISC example
Hardware Complexity:
CISC>RISC
Example: Multiplying 2 numbers
CISC: MULT B, A, C
multiplies A*C, stores result in B
RISC: ld $t0, A
ld $t1, B
prod $t3, $t0, $t1

## Slide 6: CISC vs. RISC example
The CISC architecture’s hardware performs the multiplication in a specialized circuit
The RISC architecture does not have these specialized circuits.
http://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/

## Slide 7: CISC vs. RISC
CISC Advantages
Code is simpler
Compiler does less work
Less RAM to store instructions
RISC Advantages
Hardware is simpler
therefore more registers
Uniform instruction execution time
Less register shuffling

## Slide 8: CISC vs. RISC in practice
CISC was important and necessary when hardware technology was young.
RISC developed as hardware allowed.
More when we discuss Datapath….

## Slide 9: The Assembler

## Slide 10: Assembly Qualities
Elemental Instructions
Operations only occur on Registers
Right to left assignment
Left to right evaluation
add $t0,$s1,$s2
evaluation
        assignment

## Slide 11: Assembly Program Structure
Directives
Text
Data

## Slide 12: Assembly Commands
Mnemonic - Short abbreviation for the command’s name
Cryptic
REQUIRED to comment

## Slide 13: Registers

## Slide 14: Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)

## Slide 15: Translating to Machine
Each instruction translates to a binary number
The binary number is divided into fields
Each instruction occupies one word
Two Formats:
R (register)
I (immediate)

## Slide 16: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 17: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 18: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 19: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 20: Addressing
Word – A collection of bytes
Word Size – number of bytes in a word. The word size of an architecture is constant for the entire architecture.
Unit - Memory is transferred in word sized chunks. Cannot transfer a single byte if word size is 4 bytes