## Slide 1: System Dependability
Ch 5
Professor AM Schilling

## Slide 2: System FSM
UP
DOWN
Failure
Restoration

## Slide 3: Some definitions
Availability: AKA “Uptime” when a system is able to perform and/or provide its intended service. Also known as “Service Accomplishment”
Interruption: AKA “Downtime” when a system is expected to deliver a service, but cannot.
Failure: the movement from Availability to Interruption
Restoration: the movement from Interruption to Availability
Reliability :

## Slide 4: Planning for Failure
In a perfect world, we would have no failures, but the world is not perfect!
We measure the availability of a system by deriving metrics that describe about how long we can expect the system to be up.

## Slide 5: Reliability
Reliability : the measure of uptime with respect to some time measure
Mean Time to Failure: How long before the system will fail
Annual Failure Rate: % devices expected to fail in a year for a given MTTFs

## Slide 6: Practical Calculation
Say a disk has a million hour MTTF
That’s
Which sounds like a lot, right? Mean Time to Failure is probably longer than your life span.
But it’s only Mean Time to failure

## Slide 7: Practical and Realistic, now
Annual Failure Rate looks different:
For 100,000 disks 876 can be expected to fail
= 2.4 disk/day

## Slide 8: Well, that was sobering….
….what do we do?
Plan for failure by attempting to increase MTTF
Isolate component failures so that they don’t cause a system failure
Introduce redundancy
Anticipate and possibly predict faults

## Slide 9: Specifically:
Fault Avoidance: Preventing faults by construction either through software, hardware, or a combination
Fault Tolerance: Construct system so that it handles faults gracefully. For hardware, typically done via redundancy
Fault Forecasting: Familiarity with weaknesses of system allows a component to be replaced or maintained before failure

## Slide 10: Error Detection - Parity
Parity describes the number of 1’s in a string of bits
Odd Parity – Odd number of 1’s
Even - Even number of 1’s
When a word is written to memory, an extra bit is written with it. This bit is set or unset to make the parity even

## Slide 11: Parity Example
4510 is represented as 101101
Even parity, so parity bit is 0
3110 is represented as 011111
Odd parity, so parity bit is 1
When a word is read from memory, the parity bit is checked. If parity bit does not agree with bits read from memory, an error is detected.
What’s the weakness here?

## Slide 12: Parity
4510 is represented as 101101
We store 101101 0
If we read 100101 0 , we know an error has occurred
BUT…
If we read 11011 0, do we detect an error?

## Slide 13: Hamming Code
Richard Hamming devised an error checking scheme in 1968 and was awarded the prestigious Turing Award
Hamming Distance: Minimum number of bits that are different between two bit patterns
011011 and 001111 has Hamming distance of 2

## Slide 14: Hamming Code
In the Hamming Code, we embed the parity bits
Fig 5.24
Bit positions start at one and from the left.
All power of 2 positions are parity bits
All other bits are data