## Slide 1: The Datapath

## Slide 2: Datapath
The datapath carries out instructions via the fetch/execute cycle.
It is a grouping of elements such as the ALU, a Register File, and a bus.
Processes data and addresses

## Slide 3: Goal
We will create a Datapath to implement a subset of MIPS instructions:
lw and sw
add, sub, and, or, slt (R-Types)
beq, j

## Slide 4: Executing an Instruction
  Send the program counter (PC) to the memory that contains the code and fetch the instruction from that memory
  Read one or two registers, using fields of the instruction to select the registers to read. For the lw, we need to read only one register, but most others require two registers
  … next step depends on the instruction class (what are the classes?)

## Slide 5: Types of Datapath Elements
The following slides review the two types of elements in the datapath:
Unclocked Combinational
Clocked state

## Slide 6: Combinational Elements

## Slide 7: MIPS State Elements AKA Sequential Elements
Flip-Flops ● Memories ● Registers
At any given point, the collection of State Elements characterizes the machine.
If the contents of these elements is saved to disk and the machine loses power, we can reload the data and damage from power loss would be minimized.

## Slide 8: Sequential Elements

## Slide 9: Sequential Elements

## Slide 10: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element in order to store CL results
  Longest delay determines clock period

## Slide 11: Instruction Fetch Datapath

## Slide 12: R-Format Instructions

## Slide 13: R-Type/Load/Store Datapath

## Slide 14: Branch Datapath

## Slide 15: Full Datapath

## Slide 16: Controlling the Datapath
We have the components and connections, but how do we get them to perform the proper functions depending on the instruction?
The “control” consists of the settings for components which tell it what to do.

## Slide 17: Example: ALU control
Depending on the instruction, the ALU will carry out different operations:
For an “add” instruction …well, self explanatory…
But what for a blt? What does the ALU have to do?
SUBTRACT!

## Slide 18: Example: ALU Control
Therefore, if you have an add instruction, you set the ALU to add.
If you have a blt instruction, you set the ALU to subtract. Here’s how….

## Slide 19: Applying Control to ALU
When an instruction is executed, the controls (indicated in blue) are set so that the ALU gives the appropriate result.

## Slide 20: ALU Control
Here are the ALU control settings for…
  Load/Store: add
  Branch: subtract
  R-type: depends on funct field
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 21: Determining ALU and other Control
The Datapath contains a piece of combinational logic called the Control Unit which takes the instruction as output and generates control for the components.
This control ensures the components carry out the proper tasks given the instruction.

## Slide 22: Datapath
Note that the instruction goes into the unclocked control unit. The control unit generates 7 lines

## Slide 23: Control Unit: Generating ALU Control
How do we get from the instruction to the control?
How do we get anywhere in this class?
ALL HAIL THE TRUTH TABLE!

## Slide 24: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control

## Slide 25: How is ALUOp determined?
Each Instruction has the “opcode” in the highest order bits.
This is a numeric representation of the instructions “operation”

## Slide 26: How is ALUOp determined?
The Control Unit will map the op code of the instruction to one of the four possibilities:
00
01
10
How in the world do you think THIS happens?

## Slide 28: The Main Control Unit

## Slide 29: Significance of Control Lines

## Slide 30
R-format = 0 = 000000
lw=0x32=100011
sw=0x2b=101011
be=0x4=000100

## Slide 31: R-Format Example

## Slide 32: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 33: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs

## Slide 34: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory
lw $t1, offset($t2)
sw $t1, offset($t2)

## Slide 35: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 36: CPU Overview

## Slide 37: Control

## Slide 38: Full Datapath

## Slide 39: Main Control Unit

## Slide 40: Datapath With Control

## Slide 41: R-Type Instruction

## Slide 42: Load Instruction

## Slide 43: Branch-on-Equal Instruction

## Slide 44: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode

## Slide 45: Datapath With Jumps Added

## Slide 46: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 48: Pipelining

## Slide 49: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 50: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath

## Slide 51: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 52: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 53: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 54: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 55: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3

## Slide 56: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 57: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 58: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
11 cycles
13 cycles

## Slide 59: Implementing Pipeline

## Slide 60: Datapath for Load

## Slide 61: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 62: Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 63: Assume Branch Not Taken
Predict the branch not taken and then correct the flow through the datapath in case we are wrong
  Start the execution of the next instruction
  Compute conditional for branch
  If branch is to be taken, discard next instruction by setting controls to 0

## Slide 64: Dynamic Branch Prediction
Store information pertaining to the branch – was it taken?
If it was taken last time, then assume the branch will be taken
Known as branch prediction buffer or branch history
Why is this a good scheme? Consider loops.

## Slide 65: Pipeline Control